## Slide 1: Detecting Blade Damage in Small Wind Turbines
Condition Monitoring and Fault Detection of Blade Damage in Small Wind Turbines Using Timeseries and Frequency Analyses
Thesis Defense for Luke Costello

## Slide 2: Introduction
Cal Poly Wind Power Research Center is developing LifeLine system
  A modular, low-cost condition monitoring solution for distributed wind turbines
  Necessary for safe autonomous operation
Current System:
  Monitors acceleration; no decision-making
2

## Slide 3: Project Overview
Overarching Goal:
  Develop decision-making algorithm, deploy on Cal Poly Wind Turbine
  Maximize correct alarms, eliminate false alarms
  First attempt at decision-making (simple threshold) had high false-positive rate
    Important to solve: false alarms = unnecessarily sending operators to site
3

## Slide 4: Setting Scope
Focus:
  Detecting damage to the rotor; especially the turbine blades
  Installed on Raspberry Pi
  Data logging devices:
  Raspberry Pi
    LifeLine data (acceleration)
    Controller data (control info)
  Squirrel SQ2020
    Rotor Speed
    Wind Speed
    Generator Current/Voltage
4

## Slide 5: Damage Types
Focusing on two types of damage:
  1. Mass Imbalance
    Damage that physically adds or removes mass on a blade
    Icing, lightning strikes, impacts, etc. that change blade mass
    Results in vibrations at 1X the rotor speed
  2. Aerodynamic Imbalance
    Damage that modifies aerodynamics of a blade
    Impacts, erosion, etc. that change airfoil properties
    Failure in blade pitch system
    Results in vibrations at 3X the rotor speed
5

## Slide 6: System Modifications
For proper installation, data-collection and testing, completed system changes:
Implemented integral control (~10RPM error -> ~2RPM error)
Redesigned electrical mounting unit
Automated testing system
Ryan Zhan added rotor speed, generator current and voltage sensors
6

## Slide 7: Project Setup
Testing
Design
Validation
Implementation
Characterize tower vibrational response to:
Rotor speed changes
Wind speed changes
Mass Imbalance
Collect data for algorithm validation
Develop algorithms for implementation
Evaluate algorithm performance
Tune algorithm parameters
Deploy final version on turbine
MATLAB
Python
Testing
Design
Validation
Implementation
7

## Slide 8: Testing

## Slide 9: Goals
Identify best ways to distinguish between healthy and faulty data
Determine effect of wind speed & rotor speed on tower vibrations
Collect data to verify algorithm performance
Testing
8

## Slide 10: Procedures
Testing data collected from two systems:
LifeLine
  Collected acceleration data, and later rotor speed data
Squirrel Datalogger
  Collected rotor speed, wind speed, and power output
  Data from LifeLine and Squirrel was aligned in time
Testing
9

## Slide 11: Procedures
Steady-State Tests
Rotor speed held constant for 5 minutes
Collected for 20RPM increments, 80 to 200 RPM
Ramp Tests
Rotor speed swept from 30-210RPM over 30 minute period
1RPM increment every 10 seconds
Automated testing routine
Python-based addition to control GUI
Automatically executes tests via a spreadsheet file
Testing
10

## Slide 12: Procedures
All tests completed with rotor facing approximately west
Testing
Bending Modes from Tom Gwon & George Katsanis’ theses
11

## Slide 13: Data Analysis
Testing
Two types of analyses used:
Time-series Measures:
  Describe effect of rotor speed and wind speed changes on vibrations
  Identify vibrational parameters most sensitive to damage
Frequency Measures:
  Characterize vibrational response to damage
12

## Slide 14: Time-series Measures
Root-Mean-Square:
Line Length:
Crest Factor:
Shape Factor:
Kurtosis:
Testing
Measures computed in 10s intervals for each axis of vibrations:
Used (in other research) to indicate imbalance in electric motors
13

## Slide 15: Time-series Results
Key takeaways:
Balanced rotor: Vibrations independent of rotor speed; increase with windspeed
Unbalanced rotor: Vibrations peak at 160RPM – a tower bending mode
Line Length was strongest indicator of imbalance; RMS was second-best
Testing
14

## Slide 16: Frequency Measures
Fast Fourier transform (FFT) used to describe frequency response of vibrations
Waterfall plots created to show change in frequency response with change in rotor speed
Vibrational data separated into bins of 5RPM increments
FFT of data in each bin computed via multiple 1024-point FFTs
FFT outputs in each bin averaged
Results organized into 3D mesh plot to create waterfall diagram
Testing
15

## Slide 17: Frequency Analysis
Testing
No Imbalance
16

## Slide 18: Frequency Analysis
Testing
100g Imbalance
17

## Slide 19: Frequency Analysis
Testing
200g Imbalance
18

## Slide 20: Frequency Analysis Results
Testing
Mass imbalance clearly excites the 1P frequency of vibrations
At significant enough mass imbalance, blades bent out of plane
  Resulted in aerodynamic imbalance, & 3P excitation
1P Excitation
3P Excitation
19

## Slide 21: Conclusions
Testing
Three major methods for detecting imbalances:
RMS Measure
Line Length Measure
Frequency Analysis (FFT)
20

## Slide 22: Algorithm Design

## Slide 23: Introduction
As with testing, algorithms take two forms:
  Time-series monitoring
  Frequency-based monitoring
Three algorithms pursued:
  NSET+SPRT: Time-series monitoring; designed for nuclear plants
  AFFT: Frequency-based Monitoring; designed in this thesis for wind turbines
  OFFT: Frequency-based Monitoring; designed for wind turbines
Design
21

## Slide 24: NSET + SPRT: Background
Originally developed for the Crystal River 3 Nuclear Facility
A memory-based estimation technique
NSET = “Nonlinear State Estimation Technique” - Memorized Model of Turbine
SPRT = “Sequential Probability Ratio Test” - Statistical Testing of Residuals
Design
22

## Slide 25: NSET + SPRT: Usage
10 seconds of data is processed into normalized measurement vectors:
Design
23

## Slide 26: NSET + SPRT: Training
System model is memorized by forming a memory matrix, D
Formed by selecting the most unique measurement vectors
Design
-- Sensor 1
-- Sensor 2
-- Sensor n
Time 1 --
Time 2 --
Time m --
24

## Slide 27: NSET + SPRT: Training
Building the memory matrix, D, must be done carefully:
D too small: no prediction power
D too large: matrix ill-conditioned & loses invertibility => no prediction power
D must encompass range of dataset to be estimated
Design
25

## Slide 28: NSET + SPRT: Training
Two algorithms to train memory matrix:
1. Find Extremes:
  Selects vectors with min and max values from each sensor
2. Sort by Steps:
  Sets predefined steps
  Finds vectors containing sensor values closest to these
  If the formed matrix is ill-conditioned, increases the step size and tries again
  Repeats until a suitable memory matrix is formed
Ensure D is as large as possible while still well-conditioned
Design
26

## Slide 29: NSET + SPRT: Usage
Once D is formed…
  For a new measurement vector Xobs , the estimated system state may be computed:
  W assigns a “weighting score” to each vector in D, noting similarity to Xobs
  Xest is the sum of each vector in D multiplied by it’s weighting score
  Finally, the residual is computed: = Xest - Xobs
Design
Weighting vector, W
27

## Slide 30: NSET + SPRT: Statistical Testing
Sequential Probability Ratio Test is conducted on NSET residual
  Only Y-axis Line Length residual is used for statistical testing
  Residual is assumed to be part of a normal distribution
Three hypotheses tested:
Design
28

## Slide 31: NSET + SPRT: Statistical Testing
Hypotheses tested by computing likelihood ratio:
  Probability set of rdescribed by normal distribution of parameters :
Design
29

## Slide 32: NSET + SPRT: Statistical Testing
Likelihood ratio is converted to SPRT index via:
Finally, SPRT index is compared to two thresholds, makes one of three decisions:
  Three tuning parameters: M, ,
Design
Inequality | Decision
 | System is healthy
 | More data needed
 | System is faulty
Inequality | Decision
 | System is healthy
 | More data needed
 | System is faulty
30

## Slide 33: NSET + SPRT: Algorithm Output
Design
31

## Slide 34: Adaptive FFT (AFFT): Introduction
Design
Problem:
  Frequency response of vibration signal strongly dependent on rotor speed
Solution:
  Form a unique threshold every 5RPM; compare FFT outputs to this threshold
32

## Slide 35: AFFT: Forming Thresholds
Design
Threshold Formation
  Searches a frequency response for maximum values
  Generates threshold at a fixed width around this value
Problem:
  This method has a high rate of false positives in the >10Hz region
Solution:
  Only flag faults at the 1P or 3P frequency
33

## Slide 36: Order Analysis (OFFT): Introduction
Addresses a common problem in variable-speed machinery:
  If rotor speed significantly changes over FFT duration, “smearing” occurs
    Vibration amplitudes are “smeared” across frequency response
    Can cause false positives in algorithms like Adaptive FFT
Solution:
  Resample time-series data from constant timesteps to constant angle steps
Design
Resampling
34

## Slide 37: Order Analysis (OFFT): Usage
Once vibrations are resampled, the FFT is computed
  FFT output is kept in complex vector format
  A threshold circle is formed according to:
    With Xi as training vectors at 1P and 3P frequency
Finally, new data is collected, resampled and compared
Design
35

## Slide 38: Validation

## Slide 39: Study Overview
Need:
  Assess the performance of each algorithm
  Tune each algorithm
Solution:
  Cross-Validation Study
  Selected ten healthy ramps, one 200g imbalance ramp
Validation
Healthy Data, trains algorithms
Healthy Data, tested by algorithms
Faulty Data, tested by algorithms
Run
1
2
3
:
10
36

## Slide 40: Performance Evaluation
In each run, every possible parameter combination is tested
Possible algorithm outcomes are counted:
  TP: True Positive: Alarm raised for imbalanced data
  TN: True Negative: No alarm raised for healthy data
  FP: False Positive: Alarm raised for healthy data
  FN: False Negative: No alarm raised for imbalanced data
Validation
37

## Slide 41: Performance Evaluation
Counts are formulated into several measures:
Optimal parameters are selected via an ROC chart
Validation
38

## Slide 42: Results
Validation
Tuned Algorithms:
  Operating on data > 120RPM:
Conclusion:
  None are perfect; OFFT performs worst
  Benefits of order analysis do not outweigh computation time
  Optimal algorithm would combine NSET+SPRT and AFFT benefits
 | False Positive Rate [%] | True Positive Rate [%] | F-Measure [#] | Computation Time [s]
NSET+SPRT | 0.25 | 93.3 | 0.96 | 25.8
AFFT | 0 | 69.4 | 0.82 | 11.0
OFFT | 7.14 | 72.7 | 0.80 | 78.1
39

## Slide 43: Implementation

## Slide 44: Development
Desire:
  Combine high correct decision rate of NSET+SPRT
  and zero false alarm rate of AFFT.
Solution:
  A joint monitoring approach
  NSET+SPRT: Detects something is wrong
  AFFT: Detects the exact cause (imbalances)
Implementation
40

## Slide 45: Final Version
Algorithm built into 3 Python files:
  NSET.py; SPRT.py; AFFT.py
  May be used in any Python code
First live version:
  A modified version of Ryan Zhan’s LifeLine GUI software
  Only monitoring - alarms do not stop turbine or notify off-site people
Implementation
*Simulated on faulty data
41

## Slide 46: Cross-validation
A final cross-validation study was performed on Python implementation
Results:
  False Positive Rate = 0%
  True Positive Rate = 90.2%
  F-score = 0.945
  Accuracy = 95.4%
Implementation
42

## Slide 47: Project Conclusions & Next Steps
Conclusion:
  The joint monitoring algorithm is theoretically successful
  Live version is deployed on the Cal Poly Wind Turbine
  Field testing: No false positives during normal operation
Next Steps:
  Connect algorithm to control system, for automated shutoff
  Remote notification of alarms
  Monitor other components
Implementation
43

## Slide 48: Thanks for listening! Questions?